BUILDING CONSTRUCTION

1.    Stake out (NEW HOME OR COMMERCIAL CONSTRUCTION ONLY) - before excavation.

(See attached details from the Engineering Department.)

2.    Footing - before concrete pour.

3.    Foundation/Wall - before concrete pour.

4.    Slab - before concrete pour.

5.    Backfill - after damproofing and parging.

6.    All porches, service walks, patios and garage slabs and concrete driveways - before concrete pour.

7.    A rough frame inspection is required to have rough electrical, mechanical, plumbing and grading

inspections. All roughs to be done at the same time. Commercial sites must also be inspected for

accessibility compliance at the rough stage.

8.   Insulation.

9.   Drywall - before tape or spackle.

10.   Final Inspection.  (Also see attached Engineering Department requirements)

11.   A Use and Occupancy inspection is required for new home construction and any commercial renovation

or new construction. Also see attached Engineering Department requirements. Engineering questions

may be directed to 215-633-3652. ATTENTION COMMERCIAL SITES: Final Accessibility and U&O will

be conducted only after site is fully stocked and/or partitioned and furnished.

- Fireplace - before enclosing chase (on metal chimney only).  Requires rough and final inspections.

See tank inspection information from Fire Marshal’s Office attached.

MISCELLANEOUS

- Roofing, Sheds, Siding, Electric, Plumbing, Heating/Air Conditioning, Patio and Pavers, Driveways,

Retaining Wall, Fence, Tank, or any other permit. please call 215-633-3644 for specific inspections that

may be required.

2.   All Alteration of Land Permits, (grading, drainage, piping), require Township Engineer final inspections.

To schedule a stake-out inspection, contact the Engineering Inspector 24 hours in advance at

215-633-3652. See attached for additional details. All other inspections may be requested 3 days in advance by calling 215-633-3644. You will need the permit number and job site address in order to schedule an inspection.  A responsible adult MUST BE PRESENT for all inspections. All permits and related plans must be readily available on site at the time of the inspection.  Permits are to be prominently displayed in the front window or other easily visible location.  All contractors and subcontractors are required to be properly licensed in Bensalem Township.

THE FOLLOWING ITEMS MUST BE COMPLETED PRIOR TO:

- USE AND OCCUPANCY FOR NEW CONSTRUCTION

- FINAL INSPECTIONS FOR FIRST FLOOR ADDITIONS

- FINAL INSPECTIONS FOR INGROUND POOLS

- FINAL INSPECTIONS FOR ABOVE GROUND POOLS

- Final grading completed per Township Engineer’s approved plans on

record with the Township. The grading must be smooth and any debris

must be removed prior to topsoil being distributed.

- All disturbed areas must be seeded and mulched with hay unless

property is already stabilized. Proper erosion and sedimentation control

must be installed until disturbed areas are stabilized.

- Driveways must be paved with wearing course per Township regulations.

- Splash blocks must be installed.

- Water box must be set at proper height.

- Cleanout must be set at proper height and capped.

- Service walk must be installed.

- For new homes only, curbing and sidewalks must be installed, and road

widening completed unless Township Council has approved a waiver.

- Any changes must be shown on as-built plan and submitted to Township

Engineer for review and approval.

- All subdivision requirements must be completed. The following items

may pertain to the approved subdivision plan:

  - Street trees.

  - Concrete monuments or other approved markings.

  - Road widening.

  - Storm water management systems.

11.  	All disturbed areas must be restored to original conditions.

O’Donnell & Naccarato, Inc.

Bensalem Township Engineering Department

Office 215-633-3652 ▪  Fax 215-633-3753

# Text boxes

BENSALEM TOWNSHIP

ENGINEERING DEPARTMENT

SITE INSPECTION REQUIREMENTS

LIST of INSPECTIONS REQUIRED

Rev. 11/2012

JOINING FENCE SECTIONS

Standard Filter Fabric Fence18” High

STANDARD CONSTRUCTION DETAIL

STAKE

STAPLES

* Stakes spaced at 8’ maximum. Use 2” x 2” wood or equivalent steel stakes.

Filter Fabric Fence must be placed at level existing grade. Both ends of the barrier must be extended at least 8’ up slope at 45o to the main barrier alignment.

Sediment must be removed when accumulations reach 1/2 the above ground height of the fence.

Any section of filter fabric fence which has been undermined or topped must be immediately replaced with a Rock Filter Outlet. See Standard Construction Detail #18.

6”MIN.

6”MIN. MImin.

18”

18”

FABRIC FENCE

SUPPORT STAKE*

GROUND

COMPACTED  BACKFILL

Rev. 11/2013

BENSALEM TOWNSHIP

Building and Planning Department

2400 Byberry Road Bensalem, PA 19020

215-633-3644 ▪ Fax 215-633-3753