COMMERCIAL PERMITS

1.    Footing - before concrete pour.

2.    Foundation/Wall - before concrete pour.

3.    Slab - before concrete pour.  Includes service walks, entryway, ramps, equipment pads, driveways

and parking lots in addition to general flooring slabs.

4.    Backfill - after damproofing and parging.

- A rough frame inspection is required to have rough accessibility, electrical, mechanical and

plumbing inspections. ALL ROUGHS TO BE DONE AT THE SAME TIME.

6.   Insulation.

7.   Drywall - before tape or spackle.

8.   Final Inspection.

9.   A Use and Occupancy inspection is required for any commercial renovation or new construction.

Final Accessibility and U&O will be conducted only after site is fully stocked and/or partitioned and

furnished.

If the commercial permit includes deck or pool construction, the following inspections apply:

Also consult separate inspection requirement lists for Fire Rescue and Engineering Departments

DECK

1.   Footing - before concrete pour

2.   Rough inspection

- Final inspection

INGROUND POOL

1.   Foundation (collar) - before concrete pour.

2.   Electrical bonding and backfill.

3.   Heaters - Electric, Plumbing for gas line if applicable.

4.   Final (electrical and building)

ABOVE GROUND POOLS

- Electrical - Any underground wiring (before backfill).

- Heaters - Electric, Plumbing for gas line if applicable.

- Final (electrical and building).

RESIDENTIAL PERMITS

Consult separate inspection requirement lists for Fire Rescue and Engineering Departments.

Contact BENSALEM TOWNSHIP BUILDING & PLANNING DEPARTMENT at 215-633-3644 only for FIRE RESCUE DEPARTMENT inspection scheduling as detailed on separate list.

To schedule inspections for ZONING, ALTERATION OF LAND, STAKEOUTS or other ENGINEERING inspections, contact O’DONNELL & NACCARATO ENGINEERING Inspector 24 hours in advance at

215-633-3652.

For all other residential inspections for CONSTRUCTION, INTERIOR RENOVATIONS, or projects including

Roofs, Sheds, Siding, Electric, Plumbing, Heating/Air Conditioning, Patios and Pavers, Driveways, Retaining

Walls, Fences, etc., contact CODE INSPECTIONS INC., at 215-672-9400.

MISCELLANEOUS

You will need the permit number and job site address in order to schedule an inspection.

A responsible adult MUST BE PRESENT for all inspections.

All permits and related approved printed plans must be readily available on site at the time of the inspection.

Permits are to be prominently displayed in the front window or easily visible location.

All contractors and subcontractors are required to be properly licensed with Bensalem Township before commercial permits or new home construction permits will be issued.

All contractors and subcontractors are required to be properly licensed with the Pennsylvania Attorney General’s Office before home improvement permits will be issued.

8/2014

INSPECTION REQUIREMENTS BUILDING CONSTRUCTION

- Stakeout inspection is required to be completed by the engineering department for all new homes. All required erosion and sedimentation controls must be installed prior to any earthwork activities. Any relocation must be approved by the Engineering Department.

- If underground seepage bed is required, the bed must be inspected by the Engineering Department. Several inspections may be required which will be coordinated at that time with the contractor. But initial inspection must be completed prior to installation of fabric and stone.

- A rough grade inspection is required to be completed by the engineering department for new homes only at the time of the rough inspection. All swales must be rough graded as designed as well as having base course installed on driveway.

- At the final inspection, final grading must be completed per township engineer approved plans on record with the township. The grading must be smooth and any debris must be removed prior to topsoil being distributed. Any required swales must be graded as designed on plans.

- All subdivision requirements must be completed. The following items may pertain to the approved subdivision plan:

  - Street Trees

  - Concrete monuments or other approved marking

  - Road widening (curbs and sidewalks)

  - Storm water management system

- The following are requirements that must be adhered to:

  - No grading is permitted within three (3) feet from any property line unless approved in writing on the submitted plan.

  - All disturbed areas must be seeded and mulched with hay unless property is already stabilized with an approved method. If property is not stabilized, proper erosion and sedimentation controls must be installed and maintained until disturbed areas are stabilized.

  - Any changes must be shown on a revised plan and submitted to the township engineer for review and approval.

  - A revised topographical plan may be required depending on the changes requested.

  - All disturbed areas must be restored to original conditions.

O’DONNELL & NACCARATO, INC

BENSALEM TOWNSHIP ENGINEERING DEPARTMENT

PHONE (215) 633-3652   ●   FAX (215) 633-3753

EMAIL rgans@bensalem-township.org

EMAIL qnearon@bensalem-township.org

Rev 8/2014

INSPECTION REQUIREMENTS for ALTERATION of LAND,

DECK or ZONING PERMITS

- If underground seepage bed or piping is required, the bed or pipe(s) must be inspected by the Engineering Department prior to backfill. Several inspections may be required for seepage beds which will be coordinated at that time with the contractor. But initial inspection must be completed prior to installation of fabric and stone.

- At the final inspection, final grading must be completed per township engineer approved plans on record with the township and area stabilized as required. The grading must be smooth and any debris must be removed prior to topsoil being distributed. Any required swales must be graded as designed on plans.

- The following requirements are mandatory and will be enforced:

  - No grading is permitted within three (3) feet from any property line unless approved in writing on the submitted plan.

  - All disturbed areas must be seeded and mulched with hay unless property is already stabilized with an approved method. If property is not stabilized, proper erosion and sedimentation controls must be installed and maintained until disturbed areas are stabilized.

  - Any changes must be shown on a revised plan and submitted to the township engineer for review and approval.

  - A revised topographical plan may be required depending on the changes requested.

  - All disturbed areas must be restored to original conditions.

O’DONNELL & NACCARATO, INC

BENSALEM TOWNSHIP ENGINEERING DEPARTMENT

PHONE (215) 633-3652   ●   FAX (215) 633-3753

EMAIL rgans@bensalem-township.org

EMAIL qnearon@bensalem-township.org

Rev 8/2014

THE FOLLOWING ITEMS MUST BE COMPLETED PRIOR TO:

- USE AND OCCUPANCY FOR NEW CONSTRUCTION

- FINAL INSPECTIONS FOR FIRST FLOOR ADDITIONS

- Final grading completed per Township Engineer’s approved plans on record with theTownship. The grading must be smooth and any debris must be removed prior to topsoil being distributed.

- All disturbed areas must be seeded and mulched with hay unless property is already stabilized. Proper erosion and sedimentation control must be installed until disturbed areas are stabilized.

- Driveways must be paved with wearing course per Township regulations.

- Splash blocks must be installed.

- Water box must be set at proper height.

- Cleanout must be set at proper height and capped.

- Service walk must be installed.

- For new homes only, curbing and sidewalks must be installed, and road widening

completed unless Township Council has approved a waiver.

9.    Any changes must be shown on as-built plan and submitted to Township Engineer for

review and approval.

10.    All subdivision requirements must be completed. The following items may pertain to the

approved subdivision plan:

  - Street trees

  - Concrete monuments or other approved markings

  - Road widening

  - Storm water management systems

11.    All disturbed areas must be restored to original conditions

To schedule engineering inspections, contact the Engineering Department 24 hours in advance at 215-633-3652. See attached for additional details. You will need the job site address in order to schedule an inspection. Permits are to be prominently displayed in the front window or other easily visible location.  All contractors and subcontractors are required to be properly licensed in Bensalem Township.

O’DONNELL & NACCARATO, INC

BENSALEM TOWNSHIP ENGINEERING DEPARTMENT

PHONE (215) 633-3652  ●   FAX (215) 633-3753

EMAIL rgans@bensalem-township.org

EMAIL qnearon@bensalem-township.org

1.   	Stakeout inspection is required to be completed by the engineering department for inground pools only. All required erosion and sedimentation controls must be installed prior to any earthwork activities. Any relocation must be approved by the Engineering Department.

- A rough grade inspection is required to be completed by the engineering department for

inground pools only prior to installation of concrete decking. All swales must be rough 			graded as designed.

- At the final inspection, final grading must be completed per township engineer approved 		plans on record with the township. The grading must be smooth and any debris must be 		removed prior to topsoil being distributed. Any required swales must be graded as 			designed on plans.

- The following requirements are mandatory and will be enforced:

  - No grading is permitted within three (3) feet from any property line unless 			approved in writing on the submitted plan.

  - All disturbed areas must be seeded and mulched with hay unless property is 			already stabilized with an approved method. If property is not stabilized, proper 		erosion and sedimentation controls must be installed and maintained until 			disturbed areas are stabilized.

  - Any changes must be shown on a revised plan and submitted to the township 			engineer for review and approval.

  - A revised topographical plan may be required depending on the changes 			requested.

  - All disturbed areas must be restored to original conditions.

O’DONNELL & NACCARATO, INC

BENSALEM TOWNSHIP ENGINEERING DEPARTMENT

PHONE (215) 633-3652  ●   FAX (215) 633-3753

EMAIL rgans@bensalem-township.org

EMAIL qnearon@bensalem-township.org

Rev 8/2014

# BENSALEM TOWNSHIP

Department Of Public Safety

#### FIRE RESCUE DEPARTMENT

### 2400 Byberry Road - Bensalem, Pa 19020

Phone: 215-633-3617 - Fax: 215-633-3662

REQUIRED PERMIT FIRE INSPECTIONS

| Fire Alarm System | Sprinkler System |
| --- | --- |
| 1. Acceptance Test | 1. Open Ceiling Inspection |
| 2. Central Station Report | 2. 2-Hour / 200 Pound Hydrostatic Test |
| 3. 24-Hour Battery Test | 3. Main Drain Test |
| 4. Knox Box Verification | 4. Water Flow and Tamper Valve Alarm Test |
| 5. NFPA 72 Record of Completion Report | 5. NFPA 13 Certification Report |
| Cooking Hood Suppression System | Residential Sprinkler System |
| 1. Acceptance Test | 1. Open Ceiling Inspection |
| 2. Gas/Electric Shut Off | 2. Bucket/Flow Test |
| 3. Interconnection with Fire Alarm | 3. Alarm Test |
| 4. Central Station Report | 4. NFPA Certification Report |
| 5. NFPA Certification Report |  |
| Standpipe System | Alternative Automatic Extinguishing System |
| 1. 2-Hour / 200 Pound Hydrostatic Test | 1. Acceptance Test |
| 2. Flow Test | 2. NFPA Certification Report |
| 3. NFPA 14 Certification Report |  |
| Underground Fire Main | Fire Hydrant (Installation or Repair) |
| 1. Open Ditch Inspection | 1. Open Ditch Inspection |
| 2. Hydrostatic Test | 2. Flush Test |
| 3. Flush/Flow Test | 3. Pitot Gauge/Flow Test |
| 4. NFPA 24 Certification Report | 4. Fire Hydrant Inspection Report |
| Aboveground Tank | Underground Tank |
| 1. Pressure Test | 1. Open Ditch (After Removal & After Installation) |
| 2. NFPA 704 Identification Placards | 2. Pressure Test |
| 3. Verify Approved Location | 3. Verify Approved Location |
| Fireplace, Pellet Stove, Wood Burning Stove |  |
| 1. Rough Inspection (Open Frame) |  |
| 2. Final Inspection |  |

For specific inspection information on the following permits contact Bensalem Fire Rescue:

Blasting, Environmental Site Remediation, Fireworks Displays, Hotworks/Welding, Tents

# Text boxes

BENSALEM TOWNSHIP

Building and Planning Department

2400 Byberry Road ● Bensalem, PA  19020

Office 215-633-3644 · Fax 215-633-3753

PLEASE CONSULT ATTACHED SEPARATE INSPECTION REQUIREMENT LISTS FOR FIRE RESCUE AND ENGINEERING DEPARTMENTS.

O’DONNELL & NACCARATO ENGINEERING

O’DONNELL & NACCARATO ENGINEERING

* Stakes spaced at 8’ maximum. Use 2” x 2” wood or equivalent steel stakes.

Filter Fabric Fence must be placed at level existing grade. Both ends of the barrier must be extended at least 8’ up slope at 45o to the main barrier alignment.

Sediment must be removed when accumulations reach 1/2 the above ground height of the fence.

Any section of filter fabric fence which has been undermined or topped must be immediately replaced with a Rock Filter Outlet.

18”

18”

6”MIN. MImin.

6”MIN.

GROUND

COMPACTED  BACKFILL

SUPPORT STAKE*

FABRIC FENCE

JOINING FENCE SECTIONS

STAPLES

STAKE

STANDARD CONSTRUCTION DETAIL

Standard Filter Fabric Fence18” High

O’DONNELL & NACCARATO ENGINEERING

RESIDENTIAL INSPECTIONS REQUIRED - ENGINEERING FINALS

O’DONNELL & NACCARATO ENGINEERING

INSPECTION REQUIREMENTS FOR POOL CONSTRUCTION